## Slide 1
Big Data - W2D2
Classifying Breast Tissue using Naive Bayes Approach

## Slide 2
Dataset
Dataset with electrical impedance measurements in samples of freshly excised tissue from the breast
Source
  J. Jossinet (1996) Variability of impedivity in normal and pathological breast tissue. Med. & Biol. Eng. & Comput, 34: 346-350.
  JE Silva, JP Marques de Sá, J Jossinet (2000) Classification of Breast Tissue by Electrical Impedance Spectroscopy. Med & Bio Eng & Computing, 38:26-30.

## Slide 3
Dataset
Six classes of freshly excised tissue were studied using electrical impedance measurements:
 |  | # of cases
Car | Carcinoma | 21
Fad | Fibro-adenoma | 15
Mas | Mastopathy | 18
Gla | Glandular | 16
Con | Connective | 14
Adi | Adipose | 22
 |  | 106

## Slide 4
Dataset
Attributes
  I0 Impedivity (ohm) at zero frequency
  PA500 phase angle at 500 KHz
  HFS high-frequency slope of phase angle
  DA impedance distance between spectral ends
  AREA area under spectrum
  A/DA area normalized by DA
  MAX IP maximum of the spectrum
  DR distance between I0 and real part of the maximum frequency point
  P length of the spectral curve
  Class car(carcinoma), fad (fibro-adenoma), mas (mastopathy), gla (glandular), con (connective), adi (adipose).

## Slide 5
Dataset
Case # | Class | I0 | PA500 | HFS | DA | Area | A/DA | Max IP | DR | P
1 | car | 524.8 | 0.2 | 0.0 | 228.8 | 6843.6 | 29.9 | 60.2 | 220.7 | 556.8
22 | fad | 211.00 | 0.05 | 0.09 | 30.75 | 151.98 | 4.94 | 14.27 | 27.24 | 217.13
37 | mas | 178.00 | 0.17 | 0.21 | 41.54 | 489.44 | 11.78 | 35.75 | 21.16 | 215.91
55 | gla | 470.52 | 0.13 | 0.07 | 150.22 | 2657.91 | 17.69 | 47.56 | 142.50 | 491.47
71 | con | 1724.09 | 0.05 | -0.02 | 404.13 | 3053.97 | 7.56 | 71.43 | 399.19 | 1489.39
85 | adi | 2100.00 | 0.06 | -0.05 | 390.48 | 16640.72 | 42.62 | 125.90 | 380.64 | 2073.03

## Slide 6
Dataset
Class | I0 | PA500 | HFS | DA | Area | A/DA | Max IP | DR | P
car | 524.8 | 0.2 | 0.0 | 228.8 | 6843.6 | 29.9 | 60.2 | 220.7 | 556.8
fad | 211.00 | 0.05 | 0.09 | 30.75 | 151.98 | 4.94 | 14.27 | 27.24 | 217.13
mas | 178.00 | 0.17 | 0.21 | 41.54 | 489.44 | 11.78 | 35.75 | 21.16 | 215.91
gla | 470.52 | 0.13 | 0.07 | 150.22 | 2657.91 | 17.69 | 47.56 | 142.50 | 491.47
con | 1724.09 | 0.05 | -0.02 | 404.13 | 3053.97 | 7.56 | 71.43 | 399.19 | 1489.39
adi | 2100.00 | 0.06 | -0.05 | 390.48 | 16640.72 | 42.62 | 125.90 | 380.64 | 2073.03

## Slide 7
Dataset
Class | I0 | PA500 | HFS | DA | Area | A/DA | Max IP | DR | P
0 | 524.8 | 0.2 | 0.0 | 228.8 | 6843.6 | 29.9 | 60.2 | 220.7 | 556.8
1 | 211.00 | 0.05 | 0.09 | 30.75 | 151.98 | 4.94 | 14.27 | 27.24 | 217.13
2 | 178.00 | 0.17 | 0.21 | 41.54 | 489.44 | 11.78 | 35.75 | 21.16 | 215.91
3 | 470.52 | 0.13 | 0.07 | 150.22 | 2657.91 | 17.69 | 47.56 | 142.50 | 491.47
4 | 1724.09 | 0.05 | -0.02 | 404.13 | 3053.97 | 7.56 | 71.43 | 399.19 | 1489.39
5 | 2100.00 | 0.06 | -0.05 | 390.48 | 16640.72 | 42.62 | 125.90 | 380.64 | 2073.03

## Slide 8
Dataset
Class | I0 | PA500 | HFS | DA | Area | A/DA | Max IP | DR | P
0 | 524.8 | 0.2 | 0.0 | 228.8 | 6843.6 | 29.9 | 60.2 | 220.7 | 556.8
1 | 211.00 | 0.05 | 0.09 | 30.75 | 151.98 | 4.94 | 14.27 | 27.24 | 217.13
2 | 178.00 | 0.17 | 0.21 | 41.54 | 489.44 | 11.78 | 35.75 | 21.16 | 215.91
3 | 470.52 | 0.13 | 0.07 | 150.22 | 2657.91 | 17.69 | 47.56 | 142.50 | 491.47
4 | 1724.09 | 0.05 | -0.02 | 404.13 | 3053.97 | 7.56 | 71.43 | 399.19 | 1489.39
5 | 2100.00 | 0.06 | -0.05 | 390.48 | 16640.72 | 42.62 | 125.90 | 380.64 | 2073.03
Class
Feature Vector